## Slide 1: The Bomb Lab

## Slide 2: Agenda
Bomb Lab Overview
Assembly Refresher
Introduction to GDB
Unix Refresher
Bomb Lab Demo

## Slide 3: The Elephant in the Room

## Slide 4: Downloading Your Bomb
Please read the writeup. Please read the writeup. Please Read The Writeup.
Your bomb is unique to you. Dr. Evil has created one million billion bombs, and can distribute as many new ones as he pleases.
Bombs have six phases which get progressively harder more fun to use.
Bombs can only run on your AWS servers

## Slide 5: Exploding Your Bomb
Blowing up your bomb notifies the autograder.
  Dr. Evil takes 0.25 of your points each time (every 4 explosions -1 pt)
Inputting the right string moves you to the next phase.
  Jumping between phases detonates the bomb

## Slide 6: Examining Your Bomb
You get:
  An executable
  A readme
  A heavily redacted source file
Source file just makes fun of you
Outsmart Dr. Evil by examining the executable

## Slide 7: x64 Assembly: Registers
%rax
%eax
%rbx
%ebx
%rdx
%edx
%rcx
%ecx
%rsi
%esi
%rdi
%edi
%rbp
%ebp
%rsp
%esp
%r8
%r8d
%r9
%r9d
%r11
%r11d
%r10
%r10d
%r12
%r12d
%r13
%r13d
%r15
%r15d
%r14
%r14d
Return
Arg 4
Arg 3
Arg 2
Arg 1
Stack ptr
Arg 5
Arg 6

## Slide 8: x64 Assembly: Operands
Type | Syntax | Example | Notes
Constants | Start with $ | $-42 $0x15213b | Don’t mix up decimal and hex
Registers | Start with % | %esi %rax | Can store values or addresses
Memory Locations | Parentheses around a register or an addressing mode | (%rbx) 0x1c(%rax) 0x4(%rcx, %rdi, 0x1) | Parentheses dereference. Look up addressing modes!

## Slide 9: x64 Assembly: Arithmetic Operations
mov %rbx, %rdx
add (%rdx), %r8
mul $3, %r8
sub $1, %r8
lea (%rdx,%rbx,2), %rdx
rdx = rbx
r8 += value at rdx
r8 *= 3
r8--
rdx = rdx + rbx*2
lea doesn’t dereference
Instruction
Effect

## Slide 10: Procedure Control Flow
Use stack to support procedure call and return
Procedure call: call label
  Push return address on stack
    Address of the next instruction right after call
  Jump to label (update PC)
Procedure return: ret
  Pop address of next instruction from stack
  Jump to address (update PC)
0000000000400550 <mult2>:
400550: mov %rdi,%rax # a
400553: imul %rsi,%rax # a * b
400557: retq # Return
0000000000400540 <multstore>:
400540: push %rbx # Save %rbx
400541: mov %rdx,%rbx # Save dest
400544: callq 400550 <mult2> # mult2(x,y)
400549: mov %rax,(%rbx) # Save at dest
40054c: pop %rbx # Restore %rbx
40054d: retq # Return

## Slide 11
Program counter (PC)
- stands for "instruction pointer"

## Slide 12: Return addresses

## Slide 13: Return addresses
0x40054d

## Slide 14: Return addresses

## Slide 15: TAPPS (3.32)
Registers | 
%rip | 0x400560
%rdi | 10
%rsi | 
%rax | 
%rsp | 0x7fffffffe820
*%rsp | 
?
?
?
?
?
?
?
?
?
?
?

## Slide 16: TAPPS (3.32)
Registers | 
%rip | 0x400548
%rdi | 10
%rsi | 
%rax | 
%rsp | 0x7fffffffe818
*%rsp | 0x400565
0x400565
?
?
?
?
?
?
?
?
?
?

## Slide 17: TAPPS (3.32)
Registers | 
%rip | 0x40054C
%rdi | 10
%rsi | 11
%rax | 
%rsp | 0x7fffffffe818
*%rsp | 0x400565
0x400565
?
?
?
?
?
?
?
?

## Slide 18: TAPPS (3.32)
Registers | 
%rip | 0x400550
%rdi | 9
%rsi | 11
%rax | 
%rsp | 0x7fffffffe818
*%rsp | 0x400565
0x400565
?
?
?
?
?
?
?

## Slide 19: TAPPS (3.32)
Registers | 
%rip | 0x400540
%rdi | 9
%rsi | 11
%rax | 
%rsp | 0x7fffffffe810
*%rsp | 0x400555
0x400565
0x400555
?
?
?
?
?
?

## Slide 20: TAPPS (3.32)
Registers | 
%rip | 0x400543
%rdi | 9
%rsi | 11
%rax | 9
%rsp | 0x7fffffffe810
*%rsp | 0x400555
0x400565
0x400555
?
?
?
?

## Slide 21: TAPPS (3.32)
Registers | 
%rip | 0x400547
%rdi | 9
%rsi | 11
%rax | 99
%rsp | 0x7fffffffe810
*%rsp | 0x400555
0x400565
0x400555
?
?
?

## Slide 22: TAPPS (3.32)
Registers | 
%rip | 0x400555
%rdi | 9
%rsi | 11
%rax | 99
%rsp | 0x7fffffffe818
*%rsp | 0x400565
0x400565
?
?

## Slide 23: TAPPS (3.32)
Registers | 
%rip | 0x400565
%rdi | 9
%rsi | 11
%rax | 99
%rsp | 0x7fffffffe820
*%rsp | 
?

## Slide 24: x64 Assembly: Comparisons
Comparison, cmp, compares two values
  Result determines next conditional jump instruction
cmp b,a computes a-b; test b,a computes a&b
Pay attention to operand order
cmpl %r9, %r10
jg 8675309
If %r10 > %r9, then jump to 8675309

## Slide 25: x64 Assembly: Jumps
Instruction | Effect | Instruction | Effect
jmp | Always jump | ja | Jump if above (unsigned >)
je/jz | Jump if eq / zero | jae | Jump if above / equal
jne/jnz | Jump if !eq / !zero | jb | Jump if below (unsigned <)
jg | Jump if greater | jbe | Jump if below / equal
jge | Jump if greater / eq | js | Jump if sign bit is 1 (neg)
jl | Jump if less | jns | Jump if sign bit is 0 (pos)
jle | Jump if less / eq |  | 

## Slide 26: x64 Assembly: A Quick Drill
cmp $0x15213, %r12
jge deadbeef
cmp %rax, %rdi
jae 15213b
test %r8, %r8
jnz (%rsi)
If , jump to addr 0xdeadbeef
If , jump to addr 0x15213b
If , jump to .

## Slide 27
cmp $0x15213, %r12
jge deadbeef
cmp %rax, %rdi
jae 15213b
test %r8, %r8
jnz (%rsi)
If %r12 >= 0x15213, jump to 0xdeadbeef
x64 Assembly: A Quick Drill

## Slide 28
cmp $0x15213, %r12
jge deadbeef
cmp %rax, %rdi
jae 15213b
test %r8, %r8
jnz (%rsi)
If the unsigned value of %rdi is at or above the unsigned value of %rax, jump to 0x15213b.
x64 Assembly: A Quick Drill

## Slide 29: x64 Assembly: A Quick Drill
cmp $0x15213, %r12
jge deadbeef
cmp %rax, %rdi
jae 15213b
test %r8, %r8
jnz (%rsi)
If %r8 & %r8 is not zero, jump to the address stored in %rsi.

## Slide 30: Diffusing Your Bomb
objdump -t bomb examines the symbol table
objdump -d bomb disassembles all bomb code
strings bomb prints all printable strings
gdb bomb will open up the GNU Debugger
  Things to examine while stepping through your program
    registers
    the stack
    contents of program memory
    instruction stream

## Slide 31: Using gdb
break <location>
  Stop execution at function name or address
  Reset breakpoints when restarting gdb
run <args>
  Run program with args <args>
  Convenient for specifying text file with answers
disas <fun>, but not dis
stepi / nexti
  Steps / does not step through function calls

## Slide 32: Using gdb
info registers
  Print hex values in every register
print (/x or /d) $eax - Yes, use $
  Print hex or decimal contents of %eax
x $register, x 0xaddress
  Prints what’s in the register / at the given address
  By default, prints one word (4 bytes)
  Specify format: /s, /[num][size][format]
    x/8a 0x15213
    x/4wd 0xdeadbeef

## Slide 33: sscanf
Bomb uses sscanf for reading strings
Figure out what phase expects for input
Check out man sscanf for formatting string details

## Slide 34: If you get stuck
Please read the writeup. Please read the writeup. Please Read The Writeup.
CS:APP Chapter 3
View lecture notes and homework assignments from Ch3
TA office hours: https://sites.google.com/isu.edu/cs-tutors/home/cs-tutor-schedule
man gdb, man sscanf, man objdump

## Slide 35: You got this
You should know cd, ls, ssh, and chmod by now. Use man <command> for help.
This lab also requires scp and tar
Use man <command> for help.
<Control-C> exits your current program.

## Slide 36: Bomb Lab Demo...